## Slide 1: SoftShell Calculator
O.Beketova-Hummel

## Slide 2: Start Page: the calculator consists of a single page with only Initial default values for thresholds

## Slide 3: You can select .rgp file by clicking on “Open File” button and double clicking on the file

## Slide 4: ∙ Once you select a file, its name will appear next to the “Open File” button ∙ Drill Core files are optional, and can be loaded in the same fashion ∙ It is optional to enter measured pile diameter or to change threshold values ∙ Select “CALCULATE” for each new file or set of values

## Slide 5: Once calculations are done, distance for each decay-level zone is printed for each side of the pile Based on the threshold values, “calculated diameter” value is given These measurements, as well as calculated moisture content and compression strength, can be exported via either .csv or .xlsx file by selecting “EXPORT RESULTS” button

## Slide 6: First Plot – raw data (drill and feed amplitudes), as well as Thresholds on the left (T1) and right (T2).

## Slide 7: Second Plot – drill and feed amplitudes corrected to x=0 position after zero values (marked by T1 and T2) are removed. Average lines are added.

## Slide 8: Third Plot – calculated zones are added to each side. Calculated Compression strength is added from “drill core” file.

## Slide 9: Forth Plot – calculated zones 1+2 are combined to indicate “soft Shell”

## Slide 10: Fifth plot – reported observed decay stages are added for each segment of the drill core.

## Slide 11: To save images, select “DOWNLOAD IMAGES PDF” following the last plot. A .pdf file will be saved with all plots in designated folder.