## Slide 1
Abhairaj Singh Rajendra Bishnoi Rajiv V. Joshi Said Hamdioui
Referencing-in-Array Scheme for RRAM-based CIM Architecture

## Slide 2: Motivation & Contributions
Computation-in-Memory (CIM)
Elimination of data movement
Analog computing
Emerging technologies: RRAM
  Non-volatile
  Scalable
Data as resistance states
Advantages
High parallelism
  Time complexity O(1)
High energy-efficiency
Logic & arithmetic operations
Challenges in CIM
RRAM non-idealities
  Variations
  Conductance drift
CMOS variations
RC wire parasitic
Consequences
Incorrect read
Reduced # of operands
Read disturb
Computation in Memory (CIM)
Conductance variations in RRAMs
[H. Li DATE’15]
Notes: CIM performs computation within the memory unit and thus eliminates data movement btw mem and proc.,
CIMs based on analog computing where the input and outs are analog
RRAM are promising and used in such archs, because they are non-volatile
IMAGE1 data are mapped onto crossbars as analog resistance values
However, cim faces challenges, … IMAGE2 variations during 1000 write cycle and drift with 1000 read cycles
The consequences are that we have incorrect read……

## Slide 3: Motivation & Contributions
Our Contribution
A novel binary logic computation methodology using referencing-in-array scheme
Key Attributes
High sensing margins
Adaptive to variations
Track RC parasitic
Reduced drift
Leads to
Up to 56 operands
Energy-efficiency up to 11X
Reliable up to 108 cycle (mitigated read-disturb)
State-of-the-art for Binary Logic
Dedicated sense amplifier (SA)*
External reference blocks*
Multiple cycles for multi-operand**
…
Limitations
Limited number of operands
Ignored effects of read disturb
Ignored effects of RC parasitic
**[Giannopoulos et al. AIS’21]
*[Pinatubo DAC’16, Scouting ISVLSI’17, CiM-STT TVLSI’17, MPiM ASP-DAC’17…]
Notes: Several SOTA have presented certain solutions such as … however, these solutions still face challenges such as…
In this paper, we present a novel… IMAGE1
The key attriutes of this scheme are … which will lead to …

## Slide 4: Outline
RRAM-based CIM
  Concept, Challenges
Boolean Binary Logic (BBL) in CIM
  Prior Works
Referencing-in-array scheme
  Overview, Concept, Two-operand logic, Multi-operand logic
Design for Reliability
  Concept, Two design implementations
Simulation Results
  Setup, Multi-operand validation, Impact of RC, Comparison, Overheads
Conclusion
Notes: Outline of todays presentation is as follows
We cover the concept and challeges of RRAM CIM
Prior art and existing limitaiotns
Present the concept and details of our scheme for 2 and multi-operand logic
Introduce to design solutions for better reliability

## Slide 5: RRAM-based CIM: Concept
Computation in Memory (CIM)
CIM
  → No data movement
  → Massive parallelism
Typical 1T1R RRAM Bitcell
Data maps to RRAMs
  → 0 as Low Conductance State
  → 1 as High Conductance State
RRAM
  → Non-volatile
  → Scalable (small size)
  → Compatible with CMOS
RRAM-based CIM → Massive parallelism with high energy-efficiency
Notes: The concept of CIM is that we perform computation within the memory, eliminates data movement
Moreover, several applications exploit the crossbar structure to perform multiple operation in the same cycle for eg. We can perform n logic ops in one cycle
Based on promising rram devices because they are highly scalable, compabitable with cmos in a 1t1r bitcell structure… which map the data as low and high conductance states based on presence and absence of conductive filament
Therefore..

## Slide 6: RRAM-based CIM: Challenges
Leads to
Inaccurate computations
Poor efficiency
RRAM, CMOS variations
  → PVT variations
RRAM non-idealities
  → Conductance drift
Non-ideal wires
  → RC delay mismatch
Leads to
Inaccurate computations
Limited # of reliable cycles
Leads to
Inaccurate computations
Limited CIM core size
Dealing with non-idealities is a MUST for reliable CIM
High voltage of operation
Large # of operations
Large array size
Conductance variations in RRAMs
[H. Li DATE’15]
Read disturb in RRAMs
RC delay mismatch in CIM
[H. Li DATE’15]
[W Shim IRPS’20]
Notes: However, cim face several challenges such as… which leads to
Delay mismatch due to non-ideal wires in large array CIM which leads to

## Slide 7: Boolean Binary Logic (BBL) in CIM: Challenges
Need of high margins to support large # of operands with low read disturb
*[Pinatubo DAC’16, Scouting ISVLSI’17, CiM-STT TVLSI’17, MPiM ASP-DAC’17, Giannopoulos et al. AIS’21]
…
2-Operands
00
IrefOR
IrefAND
Ic
01
10
11
Input states
Variations
IrefAND3
3-Operands
000
IrefOR3
Ic
001
010
111
Input states
011
101
110
100
Read
0
IrefR
1
Input states
Ic
Challenges
Reduced margins → Incorrect Logic Ops.
NAND bottleneck → Limited # of operands
Complex hardware → Poor Efficiency
More Challenges…
High conductance drift → Read disturb
Static approach → Limited scalability
QSA {0, 1}
G2
VR
Ic
…
GND
SA
VR•G1
G1
Gn
IrefR
CIM
VR•G2
VR
GND
IrefOR
IrefAND
MUX
IrefR
Notes: Several prior art exploit CIM as an accelerator for logic operations, here we explain is the underlying concept of perform read and logic within the cim arch.
Current read out of bitcell and reference to determine the state of the device
Now, this same concept can be used to perform logic by perform multi-row read in a cycle, if we selct say two rows, with the help of new dedicated references we can perform logic operations
Same is for 3-operands and so on
But the sensing margins are becoming small and indistguishable by the SA which leads to… ..
Therefore, there is a of having high sensing margin to support …

## Slide 8: Referencing-in-Array Scheme: Overview
**[Giannopoulos et al. AIS’21]
*[Pinatubo DAC’16, Scouting ISVLSI’17, CiM-STT TVLSI’17, MPiM ASP-DAC’17…]
Conventional*
Cascaded**
Proposed
2T2R bitcell
Differential sensing
No ext. references
Smaller, simpler SA
Multi-operand with a single dummy cell
Implement NAND with NOR
Notes: To achieve this we present a novel scheme, and here is the overview of our scheme and the changes we have as compared to prior art
Now we will present the details our scheme

## Slide 9: Referencing-in-Array Scheme: Concept
  Large margins
  Faster read
  Address RC delay mismatch
1: Set
0: Reset
BL
NBL
CSL
WL
VW
VW
GND
GND
GND
VW
Cell Structure
…
…
QSA
QSA
VDD
0.2um
1.6um
1.6um
BL
NBL
CSL
SAE
1.6um
0.2um
SA
1.0um
0.46um
Read Operation
△V=40mV
△V=80mV
40% reduction in WL
Notes: Our schems is based on a 2t2r cell structure where the data and complementary data is stored as shown
A cell like this can be programmed in a similar way as 1t1r, with a common source line.
We define SET state as HCS on the left BL side and LCS on the right NBL side
With such a cell structure, we can perform read in a similar fashion as SRAMs, we select a row… develop voltage diff at the bitlines, sensed by SA to give a read output.
The adv,. Of the approach is that we have more than 2x sensing margin which we can arrive at at an faster time, assuming SA requirement is 40mv, the conv. Scheme in 1t1r cell…
Now, in order to perform logic we need to make some modifications, and the modifications are explained as follows…

## Slide 10: Referencing-in-Array Scheme: Two-Operand Logic
Dummy cell →
  Both devices are High Conductance State
  Separate WL for NAND, NOR
1
Idea
→ For NOR, we bias BL with ION
→ For NAND, we bias NBL with ION
In | IBL | INBL | Out
00 | ION | 2ION | 1
01 | 2ION | ION | 0
10 | 2ION | ION | 0
11 | 3ION | 0 | 0
BL
NBL
CSL
WLNOR
WLNAND
WLNOR
WLNAND
ION
2ION
…
…
BL
NBL
CSL
IBL
INBL
WL
NOR (0,0)
0
In | IBL | INBL | Out
00 | 0 | 3ION | 1
01 | ION | 2ION | 1
10 | ION | 2ION | 1
11 | 2ION | ION | 0
WLNAND
2ION
ION
…
…
BL
NBL
CSL
WLNOR
IBL
INBL
WL
NAND (1,1)
+
+
Assumptions →
  ION >> IOFF or IOFF=0
2-Operand NOR
2-Operand NAND
Notes: We introduce a dummy cell at the top of the crossbar with both…
Sepeate…
We assume..
And the idea is to bias bl with ion
For nor op. we enable wl nor and disable.. And we determine the currents responsible for discharging the bitlines..
Similar we perform for our input states and get this table
Similarly for nand we enable nand wl, disable …
Similar we perform for our input states and get this table

## Slide 11: Referencing-in-Array Scheme: Two-Operand Logic NAND
  Allows large margins
  Faster read (~ 2X gain)
  Address RC delay mismatch
  Same SA
  NAND is not a bottleneck anymore
Notes: Here we compare the timing requirement of scheme with signle ended sensing in conv. Since we arrive at required margin at a early stage, we gain in speed.
Hence this approach allows..
Since we perform nor nand with the same worst case,
But can we use this scheme for multi-operands going forward?? Lets see

## Slide 12: Referencing-in-Array Scheme: Multi-Operand Logic?
Possible Idea
→ For 3-NOR(NAND), we bias BL(NBL) with 2ION
→ For 4-NOR(NAND), we bias BL(NBL) with 3ION …
In | IBL | INBL | Out
000 | 2ION | 3ION | 1
001 | 3ION | 2ION | 0
010 | 3ION | 2ION | 0
001 | 3ION | 2ION | 0
011 | 4ION | ION | 0
101 | 4ION | ION | 0
110 | 4ION | ION | 0
111 | 5ION | 0 | 0
3-Operand NOR
1
2ION
3ION
…
…
BL
NBL
CSL
WLNOR
WLNAND
IBL
INBL
WL
NOR (0,0,0)
+
+
WLNOR
WLNAND
…
4 array bitcells
3 dummy cells
4-Operand NOR
5 array bitcells
4 dummy cells
5-Operand NOR
Expensive for higher operands
Notes: For 3-operand, we need to 2 dummy cells, we can perform with the same mechanism, and for 4.. 3 dummy cells.. For 5..
Here the idea is to…
but this approach can lead to..
Hence we need a new approach

## Slide 13: Referencing-in-Array Scheme: Multi-Operand Logic
Dummy cell → WLs are degraded
Array cell → WLs are separated
NOR | NAND
WLNOR- | WLNAND-
WD | WDB
(n)IOFF
WL--NAND
WL--NOR
…
…
…
…
ION+(n-1)IOFF
Iref
Iref
WLDB<1>
WLD<1>
WLDB<2>
WLD<2>
…
…
…
…
…
WLDB<n>
…
WLD<n>
NOR (0,0,0…0)
NOR (1,0,0…0)
1
0
GND
VDD
WLNOR--
MEN1
WLNAND-- = 0
MEN2
MEN1, MEN2 | NOR logic (WLNOR--)
00 | VDD – △V1 – △V2
01 | VDD – △V2
10 | VDD – △V1
11 | VDD
Calculate Iref
(For e.g., 3-16 Operands)
Worst cases →
  0,0,0…0 ~ 16*IOFF
  1,0,0 ~ ION + 2*IOFF
Iref should be in the middle
For e.g., up to 16-operand NOR,
  Iref =
+
+
Notes: Here we introcude a novel scheme to operate with any arbitrary operand size,
First we need a few modifications.. First…
Now we can perform in a similar way with an iref which fall perfectly in between the critical states of all zeros (reset) and one 1 and rest zeros (reset)
We calculate this conductance states with the following approach example with 3-16 operands..
How we achieve this state is using a bleeder circuit, we short the the dummy word line and by voltge divieder we can tune to a lower wl voltage level
We can perform nand by…

## Slide 14: Referencing-in-Array Scheme: Multi-Operand Logic
  Single reference for arbitrary NAND, NOR
  Smaller margins are avoided
  Address RC delay mismatch
  Same SA
  Multi-operand is not a bottleneck anymore
Notes: Here we compare the timing requirement of scheme with our 2-input approach.
We see that we some additional time, we arrive at the desired bl voltage diff for the SA
Hence this approach allows..
Since we perform nor nand with the same worst case, nand is not a problem, as well as multi-opernd

## Slide 15: Design for Reliability: Concept & Design Implementations
Read Disturb
Unwanted bit-flip due to
More # of operations
High voltage of operation
Solution
Reduce the # of operations
Reduce voltage of operation
Circuit Design
Allow more operations (multi-operands) in a single cycle
Pre-charge (DFR-P) or pre-discharge (DFR-N) to a lower voltage
DFR-P
DFR-N
Timing Diagrams: Configurable voltage levels achieved with configuring the duration of BLDIS signal
V
300ps
500ps
Notes: In order to have reliable cycle agiaanst the possibility of read disturb, we investigate the causes and accelertors of read distub
Solution could be..
Our solution
The circuits … now how much time we discharge it is our hands
The timing digram to validate this circuit is shown here, for two easily configurable times
here we name 300 as fast operations
So, we see here that by investiting some time before the start of the cycle, we settle the bls at a desired lower voltage to reduce read disturb.
And the equilizer will help us to stabilize the two bls at the same voltage level
Now, we present resukts to validation our designs and compare our effiency compared to prior arts,

## Slide 16: Simulation Results: Setup
RRAM Bitcell | Specifications
RRAM device | HfO2/TiOx [Kim Nature‘16]
HCS / LCS | 100KΩ / 3KΩ
RRAM variations | 20% (parametric)
Bitcell Config. | 2T2R
Pass Transistor | 540nm / 40nm
BL (WL) res. /bitcell | 0.4Ω / 0.8Ω
BL (WL) cap. /bitcell | 0.3fF / 0.6fF
Simulation Platform | Specifications
Simulator | Cadence Spectre
Simulator Version | MMSIM_14.10.765
Voltage supply | 0.9V 10%
CMOS | RVT, 40nm TSMC (3)
Temperature | -40℃ to 125℃
Simulation Platform | Specifications
Simulator | Cadence Spectre
Simulator Version | MMSIM_14.10.765
Voltage supply | 
CMOS | 
Temperature | -40℃ to 125℃
CIM Core | Specifications
Crossbar size | 512x512 (256 Kb)
Sense Amplifier (SA) | 5T voltage-based
SA min. sensing margin | 40mV
Notes: Here is the simulation setup we used
Details of the simulator,
Cmos models
Rram models
Variation considerations and res. Cap per pitch used,

## Slide 17: Simulation Results: Multi-operand Validation
  Margins diminishes with ION currents
  We only deal with IOFF currents
Limitation of the Conventional scheme
We enable up to 56-operand logic compared to 4-operand in a single cycle
Proposed scheme
m(opr) →
# of operands (m)
# of SET devices (opr)
Notes: In this slide we explain that how prior can not perform above a certain operands size, and how is it possible for us to perform large numbe rof operands.
Since the conv. Sechme works with ion currents for nand operations, because of limited voltage range and it can not arrive to having required SA margins after a acertain numer fo operands
The voltage at the bl all converge, getting to close to each other, and margins are not enough for realible logic operations
Since we work with off currents , we have a lot of marign btw the two critical states,
And with reconfigurable refernces we can go up to large nunmebr of operands, here, with res. Ratio of 33, and cnfgurable refefcen we can perform up to 56 opernads
A higher ratio can lead to even higher # of operands
So n conclusion,…

## Slide 18: Simulation Results: Impact of RC
  Non-static reference improves scalability
  Sensing margin Degradation rate is improved
  Similar RC for each cell
Sensing margin degradation
Column index
WL degradation
m(opr) →
# of operands (m)
# of SET devices (opr)
Notes: Reagridn rc delay, the problem arraises from high number of opernds as explained in the previous slide and, rc delay mismatch
Here wl degradaaton with rising number of columns along a row can lead to weak pass gates and undesired bl current drops
And with static refernces, like in conv, schem the desird margins vanishes and we hve incorrect read.
In our prospoed shcems, since our dummy cell generating reference is in every column, it suyffers from similar degradation cand therefore can adapt to rc delays
And sicne we avoid ion currents, we aonly concern with all zeors and one one, we aoid this small margins,.
Now we compare our schem for efficny

## Slide 19: Simulation Results: Comparison
11X gain
in performance & energy-efficiency
Up to 108 reliable cycles, compared 102 cycles traditional approach
Latency Comparison
Reliability analysis
Notes: In terms of latency
We assume sim ialr sa, decode, so similar power,
We assume similar analysis for energy gain
We compare with 2 approaches one withc can not go beyond 4 operands,
one cascacdede wihere we do 2-inuts operands at a time, accumulate results in every cycle and do multi-input logics in multi-ccyles
Here we see as # of operands increase we gain more in terms of speed and energy , with max. at the highest hat wew can support here 56 with 11x gain in speed and energy
We also did analysis on the gain number of reliable cyekls using our deisng for relaibilrity approach
Here if we invest more time, we can reduce the starting point of the bls, reduce read disrb posssibilty and gain in the bumber for realible cycles on the same operands.
We can reachj upto 108 cycles by investing say 600ps…

## Slide 20: Simulation Results: Overheads
1T1R in the conventional schemes
2X (1T1R) in the conventional schemes
2T2R in our proposed scheme
~2X bitcell area (overall CIM ~1.67X due to smaller periphery)
Notes: The adv. Presented in this paper comes with some additional area, as 2t2r can lead to 2x bitcell area,
Since we reduce peripeher, no generators etc., simpler SA, penalty is reduced to 67% ,more area
Summarizes the pros. And cons.. We have…

## Slide 21: Conclusion
Read-assisted BBL designs in CIM architectures
  Challenges: RRAM non-idealities, CMOS variations, RC parasitic…
Conventional approaches are inefficient
    Small sensing margins in NAND → Degraded accuracy, limited scalability
    Limited number of operands → Poor accuracy, performance & energy-efficiency
    Reference generators/large SA → Poor performance & energy-efficiency
    RC wire parasitic → Degraded accuracy with RC parasitic
    Read disturb → Limit the number of reliable cycles
    Proposed referencing in array scheme exhibits superiority
  2T2R-based differential sensing scheme using a dummy bitcell row
    Can support 56-operands per cycle compared to four-operands
    Up to 11X improvement in performance and energy-efficiency
    Improve the scalability of functional crossbar size
    Orders of magnitude improvement in the number of reliable cycles
    Takes up to 67% more area
Notes: In summary, rram cim attractive with face challegnes suych as
conv. Scheme suffer from
And our proposed sche, offers 56…

## Slide 22
Thanks!!
Abhairaj Singh Rajendra Bishnoi Rajiv V. Joshi Said Hamdioui
Referencing-in-Array Scheme for RRAM-based CIM Architecture
This work was supported in part by the EU H2020 grant “DAIS” that has received funding from the ECSEL Joint Undertaking (JU) under grant agreement No 101007273.