## Slide 1: FLORIDyn 3.1
A dynamic and flexible framework for real-time wind farm control Software guide
Marcus Becker

## Slide 2: Content
Run a simulation
Create a new simulation
  Create a layout
  Create inputs
Use SOWFA data
  As inputs
  As validation

## Slide 3: Run a simulation

## Slide 4: Run a simulation
Open main.m
Modify pathToSimulation to a folder name in .\Simulations (e.g. ‘2021_9T_Data’)
Run main.m

## Slide 5: Create a new simulation

## Slide 6: Create a simulation – Part 1: Folder
Create a new folder in .\Simulations with a desired name
Copy the contents of .\Simulations\0000_Source into your new folder.
Open .\Simulations\your folder\turbineArrayProperties.m to create a wind farm layout and set initial turbine states.
Open .\Simulations\your folder\setup.mlx to set various settings for the simulation. Note: if you do not have the option to use .mlx files, use setup_plain.m and rename it to setup.m. It offers the same functionality but with no drop-down menus for safe inputs.

## Slide 7: Create a simulation – Part 2: Setup
.\Simulations\your folder\setup.mlx sets the
Simulation settings,
  Start / end time, time steps, rotor discretization, initialization, dynamic settings (advection & OP propagation model)
Controller settings,
  Currently limited to external yaw input
Flow conditions,
  Wind velocity, direction, shear and ambient turbulence intensity input
State correction,
  How the OP flow field states are changed
Wind Field state perturbation / noise
  Random per time step change of the flow field state
Visualization
  2D, 3D flow field plots, online, post-sim, power generated, effective wind speed etc.

## Slide 8: Create a simulation – Part 3: Inputs
Depending on what inputs you chose in setup, you’ll need the according files in .\Simulations\your folder\Data .
.\Simulations\0000_Source\Data has some examples, usually you need a .csv which is called Wind___ ____.csv – where the first empty part is Control_, Dir, Vel, TI, Shear depending on what you want to set and the second part is the input mode (Interpolation is assumed as default and has no second part.).
If you request an input source and you do not have the suitable input file, the code will throw an error and will generate an input file for you to modify.
Generally the data is assembled in [time, value T0, value T1, … , value Tn] rows. See the example files for inspiration.

## Slide 9: Run the simulation!
Open main.m
Modify pathToSimulation to a folder name in .\Simulations (e.g. ‘2021_9T_Data’)
Run main.m

## Slide 10: Use SOWFA data

## Slide 11: Use SOWFA data as input
SOWFA data can currently be used as an input to set the yaw angle and as input for the I&I estimator.
Move the needed files from the SOWFA folder .\postProcessing\turbineOutput\*\ into .\Simulations\your folder\Data
  For yaw you’ll only need the nacelleYaw file
  For the I&I estimator you’ll need bladePitch, generatorTorque, rotorSpeed (or rotorSpeedFiltered)
Rename the files from *name* to SOWFA_*name*.csv
  The bladePitch file sometimes includes the expression “3{0}” for the data, where 0 is the pitch value. Find and remove all “3{” and “}”.

## Slide 12: Use SOWFA data as input
You can now select
Wind.Input_Vel = ‘I_and_I’;
  You still need the wind speed estimator parameters, stored in the WSEParameters.m file which you can find in .\Simulations\0000_Source\
Con.Yaw = 'SOWFA‘;

## Slide 13: Use SOWFA data as validation
SOWFA data can also be used as comparison and validation. This can be done with the power generated and the flow field.
Move generatorPower from the SOWFA folder .\postProcessing\turbineOutput\*\ into .\Simulations\your folder\Data and rename it into SOWFA_generatorPower.csv. It will be now automatically used in the power generated plots.
To compare the flow fields store the path to the SOWFA folder .\sliceDataInstantaneous in Vis.FlowField.Error.ValidationPath in \Simulations\your folder\setup.mlx (at the very end) and enter the name of the snapshot (e.g. U_slice_horizontal). Check the Vis.FlowField.Error.Online box in setup.mlx (set the value to true). The simulation will now check if there is a SOWFA folder with the current time step and will then generate an error plot, which is stored in \Simulations\your folder\Results\ErrorVTK\ Note that plotting is resource intensive and the simulation will run significantly longer.

## Slide 14: Resources
[1] The revised FLORIDyn model: Implementation of heterogeneous flow and the Gaussian wake, M. Becker, B. Ritter, B.M. Doekemeijer, D. van der Hoek, U. Konigorski, D. Allaerts and J.W. van Wingerden, 2022, Wind Energ. Sci. Discuss. [preprint], in review
[2] Experimental and theoretical study of wind turbine wakes in yawed conditions
M. Bastankhah and F. Porté-Agel, 2016 J. Fluid Mech., vol. 806, pp. 506-541.
[3] A Control-Oriented Dynamic Model for Wakes in Wind Plants P.M.O. Gebraad and J.W. van Wingerden, 2014 J. Phys.: Conf. Ser. 524 012186
[4] The Immersion and Invariance Wind Speed Estimator Revisited and New Results Y. Liu, A. K. Pamososuryo, R. M. G. Ferrari, J.W. van Wingerden 2022 IEEE Control Systems Letters
[5] Partition of the circle in cells of equal area and shape, L. Masset, O. Brüls and G. Kerschen, 2011
[6] Simulator for offshore wind farm applications, National Renewable Energy Laboratory, 2022, GitHub
Marcus.Becker@tudelft.nl